## Slide 1
EE 371
MICROELECTRONIC DEVICES AND CIRCUITS

## Slide 2: Outline
Introduction to Operational Amplifiers
Basic Amplifier Characteristics
Modeling the Op-Amp
Basic Applications Of The Op-Amp
Differential Amplifiers
Non-ideal Characteristics Of Op-Amps

## Slide 3: Introduction to Operational Amplifiers
Operational Amplifiers (OpAmps)
One of the primary active devices in analog electronics, second only to transistors.
Used in low and intermediate frequency applications.
Widely accepted due to their usefulness, predictability, and cost-effectiveness.
Fundamental for learning electronics circuit design and analysis.
What Makes OpAmps Important?
Easily configurable for various linear and non-linear functions.
Originally developed with vacuum tubes, now integrated as transistorized circuits.

## Slide 4: Applications And Concept of Opamps
Common Applications:
Signal Processing: Filters, limiters, synthesizers.
Communication Circuits: Oscillators, modulators, phase-locked loops.
Analog/Digital Conversion: A/D and D/A converters.
Mathematical Operations: Multipliers, dividers, adders.
Concept:
OpAmps are building blocks described by their terminal characteristics.
Can be modeled using resistors, capacitors, and voltage sources
Foundation for circuit design by interconnecting active and passive components.

## Slide 5: Basic Amplifier Characteristics
An amplifier is a device that increases the amplitude of a signal without significantly altering its waveform
Amplifiers are essential in electronic systems for signal processing, communication, and control systems.
Gain
Definition: The ratio of the output signal amplitude to the input signal amplitude.
Formula:
Where is the gain, is the output voltage, and is the input voltage.

## Slide 6: Basic Amplifier Characteristics
Types of Gain:
Current Gain:
Amplifier Characteristics
Linearity: The output is directly proportional to the input within a specified range.
Bandwidth: The range of frequencies over which the amplifier maintains a consistent gain.
Efficiency: The ratio of output power to total power consumed.
Impedance Matching:
  Input Impedance (Rin): Should be high to prevent loading the source.
  Output Impedance (Rout): Should be low to drive loads effectively

## Slide 7
An amplifier introduces a time delay between input and output signals due to propagation through internal components.
The relationship is given by:
where
is the gain,
is the input signal,
is the output signal,
is the time delay,
is the output DC offset
Saturation and Limitations
Power Supply Limitation: The maximum output voltage is constrained by the power supply voltage.
Saturation: The output cannot exceed the power supply range.
Current Limitation: The output is limited if the power supply cannot provide sufficient current.
An amplifier has an open-loop gain of 200,000 and an input voltage of 1mV. Calculate the output voltage if the amplifier operates within its linear range.
Solution,

## Slide 8
Common OpAmps
µA741 (LM741, MC1741): Most commonly used general-purpose OpAmp.
OP-27, LF411: High-performance OpAmps.
LM324: Single-supply OpAmp.
Practical Considerations
Input and Output Impedance:
  High input impedance prevents loading effects.
  Low output impedance ensures strong signal delivery.
Noise and Distortion: Minimize external noise sources and maintain linear operation.

## Slide 9: Modeling the OpAmp
Modeling an operational amplifier (OpAmp) involves understanding its terminal voltages, currents, and behavior under different configurations.
Non-inverting Input (V⁺): The voltage applied to the non-inverting terminal.
Inverting Input (V⁻): The voltage applied to the inverting terminal.
Output Voltage : The resulting voltage at the output terminal.
Power supply voltages: (positive rail) and (negative rail)

## Slide 10: Voltage and Current Constraints
Voltage Constraints:
The ideal OpAmp follows the equation:
where:
is the open-loop gain, which is ideally very large.
The output voltage is limited by the power supply:
If reaches these limits, the OpAmp is said to be saturated.

## Slide 11
The Virtual Short Concept
In the linear operating region, the OpAmp enforces:
Ideal OpAmp Assumptions
For analysis and circuit design, an ideal OpAmp is assumed to have:
  Infinite open-loop gain )
  Infinite input resistance )
  Zero output resistance )
KEY NOTE:
OpAmp behavior is characterized by terminal voltages and currents.
The output voltage is proportional to the input difference but limited by power rails.
Ideal OpAmps assume infinite gain, infinite input resistance, and zero output resistance.
Circuit theory concept.
The virtual short concept simplifies circuit analysis.

## Slide 12: BASIC APPLICATIONS OF THE OPAMP
Operational amplifiers (OpAmps) are widely used in various circuit configurations to perform fundamental signal processing functions such as amplification, summation, integration, and differentiation.
We will treat the following OpAmp application:
  Inverting Amplifier
  Summing Amplifier
  Non-Inverting Amplifier
  Difference Amplifier
  Integrator
  Differentiator

## Slide 13: Inverting Amplifier

## Slide 14
Question 1
Vin=2Vsint
R1=800Ω
Rf=1200Ω
V
t
Vout=?

## Slide 15
Question 2
For the circuit shown below:
Determine the gain of the amplifier if Vi=2sin⁡ωt V.
Find the output voltage.
Calculate the input voltage amplitude that will cause the amplifier to saturate.

## Slide 16: Non-Inverting Amplifier

## Slide 17: Question 3 and 4
Find
a) If Rx=80kΩ what is Vo
b) How large can Rx be to avoid saturation

## Slide 18: Summing Amplifier
A very important application of the inverting configuration is the weighted-summer circuit shown in the Fig. Here we have a resistance Rf in the negative-feedback path (as before), but we have a number of input signals v1, v2, …, vn each applied to a corresponding resistor R1, R2, …, Rn, which are connected to the inverting terminal of the op amp.

## Slide 19: Question 5
Two voltage signals, Vi1= 2V and Vi2=1.5V are added by the summing amplifier in the figure below.
Find the output voltage, Vo.

## Slide 20: Difference Amplifier
A difference amplifier is one that responds only to the difference between the two signals applied at its input

## Slide 21: Question 6
.

## Slide 22: Question 7
Find Vo

## Slide 23: Integrator
Output Voltage Derivation
Using KCL at node 1:
Since, simplifying:
Solving for
This circuit is used in analog computing and signal processing.
A resistor is connected to the input.
A capacitor is placed in the feedback loop
.

## Slide 24: Differentiator
Output Voltage Derivation
Applying Kirchhoff’s Current Law (KCL) at the inverting terminal:
Using the voltage constraint
e output voltage is therefore,
This shows that the output is the derivative of the input.
Applications
  Edge detection in signal processing
  High-pass filtering in audio circuits.
A capacitor is connected to the input.
A resistor is placed in the feedback loop.
The non-inverting terminal is grounded.

## Slide 25: Differential Amplifiers
A Differential Amplifier is an essential circuit in analog electronics that amplifies the difference between two input signals while rejecting common-mode noise.
It forms the foundation of many advanced circuits, including instrumentation amplifiers.
Key Features
Amplifies the difference between two input signals.
Rejects common-mode signals (same signal on both inputs).
Used in signal processing, sensor applications, and audio circuits.

## Slide 26: Differential Amplifiers
Working Principle
.
.
The feedback network maintains balance.
The output is proportional to
To analyze the circuit, we apply Kirchhoff’s Laws and Voltage Division.
Voltage at Inverting Input (
Using the voltage divider rule:
Since the OpAmp operates in a closed-loop configuration, the virtual short principle applies, meaning the voltage at the non-inverting input is equal to
At node 1,

## Slide 27: Differential Amplifiers
Substituting :
Solving
If the resistor pairs are equal , the gain simplifies to:
This means the amplifier scales the voltage difference by a constant factor.

## Slide 28: Differential Amplifiers
One of the most important properties of a differential amplifier is its ability to reject common-mode noise.
Common-Mode Gain ()
If both inputs have the same voltage:
Then the output should ideally be zero. However, due to imperfections:
CMRR Definition
The Common-Mode Rejection Ratio (CMRR) is given by:
A higher CMRR means better noise rejection.
Practical Applications
Differential amplifiers are widely used in:
  Instrumentation Amplifiers: High-precision measurement circuits.
  Audio Systems: Removing unwanted noise and interference.
  Communication Systems: Signal processing in radio receivers.
  Sensor Signal Conditioning: Extracting weak differential signals from sensors.

## Slide 29: Question 8
.
The difference amplifier of Figure 1.20 is constructed with an ideal OpAmp and 1% tolerance resistors of nominal values 2.2 kand 5.1k The resistors were measured and found to have the following resistance values: =2.195 k, k
Determine gain of the differential amplifier and its common-mode rejection ratio.
Figure 1.20

## Slide 30: NON-IDEAL CHARACTERISTICS OF OPAMPS
OpAmps exhibit non-ideal characteristics that can significantly impact circuit performance.
Why Study Non-Ideal Characteristics?
Understanding OpAmp imperfections helps engineers:
Design accurate and stable circuits.
Minimize errors due to input offsets and bias currents.
Optimize performance for speed and frequency response.
Reduce noise and unwanted interferences.

## Slide 31: Non-Ideal Characteristics of OpAmps
In an ideal OpAmp, we assume:
Infinite voltage gain
Infinite input resistance
Zero output resistance
No offset voltage or input bias currents
Independent of frequency response and power supply variations
However, real-world OpAmps exhibit non-ideal characteristics, which impact circuit performance. These include:
Finite Gain
Finite Input Resistance
Non-Zero Output Resistance
Input Offset Voltage & Bias Current
Limited Frequency Response
Slew Rate Limitations
Power Supply Limitations

## Slide 32: Finite Gain, Finite Input Resistance, and Non-Zero Output Resistance
This section analyzes how real OpAmps deviate from ideal models, particularly in closed-loop configurations like the inverting amplifier.
We apply KCL at the inverting input node:
Since virtual short is not exact in a non-ideal OpAmp, we define ​ in terms of open-loop gain
Since (grounded non-inverting terminal),
.

## Slide 33: Finite Gain, Finite Input Resistance, and Non-Zero Output Resistance
Substituting ​​ into KCL Equation
Multiplying by to clear fractions:
Solving for gain:

## Slide 34: Finite Gain, Finite Input Resistance, and Non-Zero Output Resistance
.
This shows that finite gain reduces the actual closed-loop gain compared to the ideal case

## Slide 35: Finite Gain, Finite Input Resistance, and Non-Zero Output Resistance
A real OpAmp has a small but nonzero which affects output voltage when a load ​ is connected.
Applying voltage division at the output:
Thus, the final closed-loop gain including is:
This equation shows how finite gain, finite input resistance, and nonzero output resistance collectively degrade the gain.
.

## Slide 36: EQUIVALENT CIRCUIT

## Slide 37: Question 9
Given the following circuit parameters for an inverting amplifier, Rf=20kΩ, Rs=10kΩ, Vs=2V and non-ideal OpAmps parameters: A=200,000, Ri=2MΩ, Ro=50Ω. Draw the circuit and Determine the voltage gain of the amplifier and compare to the ideal gain.

## Slide 38: CASCADED OP-AMPS
Multistage configuration of amplifiers interconnected in sequence
Cascaded amplifiers are amplifier stages connected one after another, where the output of one stage becomes the input of the next stage.
They are used when:
A single amplifier cannot provide enough gain
Different stages are needed for voltage gain, current gain, or impedance matching
Better control over frequency response and stability is required
For proper cascading:
Output impedance of first stage should be low
Input impedance of next stage should be high
This prevents signal loss due to loading effect.

## Slide 39: Question 10
Find Vo
Design Vo=3V2-5V1